## Slide 1: Chapter 5 Discrete-Time Fourier Transform

## Slide 2: Discrete-Time Fourier Transform ≠ Discrete Fourier Transform (DFT)

## Slide 3: Outline
From Discrete-Time Fourier Series to Discrete-Time Fourier Transform
DT FT of Periodic Sequences
DT Fourier Transform Properties
System Characterized by Difference Equations
Discrete-Time Processing of Continuous-Time Signals (Chapter 7)
Sampling of Discrete-time Signals (Chapter 7)

## Slide 4: Recall: DT LTI System Response to
Assume LTI system with impulse response h[n]
Recall sum convolution:
System response to
Let
zn eigenfunction, H(z) eigenvalue
If , then
§5.1 DT FS to DT FT

## Slide 5: Recall: Fourier Series of DT Periodic Signals
Recall: x[n] is periodic if x[n]=x[n+N]
Fundamental period: the smallest positive N
Fundamental frequency: ω0=2π/N
DT complex exponential signals with period N
Only N distinct signals in the above set
linear combination of x[n]
§5.1 DT FS to DT FT

## Slide 6: From DT FS to DT FT (1)
x[n] is a sequence with finite duration: x[n] is not zero only in the range of –N1≤n ≤N2
Construct a periodic signal : x[n] is one period of
§5.1 DT FS to DT FT

## Slide 7: From DT FS to DT FT (1)
x[n] is a sequence with finite duration: x[n] is not zero only in the range of –N1≤n ≤N2
Construct a periodic signal : x[n] is one period of
Fourier series representation of
Relate the FS coefficients to
§5.1 DT FS to DT FT

## Slide 8: From DT FS to DT FT (2)
FS coefficients
are the sampled values of at the frequency points of in which
Define a frequency-domain function
,
§5.1 DT FS to DT FT
Q: Why not use X(ω) or X(jω)?

## Slide 9: From DT FS to DT FT (3)
Note that
When N∞, x[n] , summation becomes integral
Discrete-time Fourier transform pair
§5.1 DT FS to DT FT
Analysis equation
Synthesis equation
Q: x[n] has to be finite duration?
A: No.

## Slide 10: DT FT Example
§5.1 DT FS to DT FT

## Slide 11: is Periodic!
The fundamental period of is 2π
§5.1 DT FS to DT FT
Q1: What is the period of X(jω)?
Q2: The real meaning of 2π in the horizontal axis of X(jω) plot?

## Slide 12: Periodic Signal vs. Aperiodic Signal x[n]
FS coefficients of are the equally spaced samples of
This is the basis of Discrete Fourier Transform (DFT)
  discrete in both the time domain and the frequency domain
§5.1 DT FS to DT FT

## Slide 13: Examples of DT FT
Example 5.1,
Example 5.2
§5.1 DT FS to DT FT
Q1: How to find magnitude and phase of X(jω)?
A: Draw the complex plane
a=0.5
a=-0.5
real + even  even + real

## Slide 14: DT FT of Rectangle Pulse
§5.1 DT FS to DT FT

## Slide 15: Convergence of DT FT
Recall: No convergence problem for DT FS.
No convergence problem for DT FT of sequences of finite duration.
How about sequences of infinite duration?
  convergence of analysis equation: conditional
  synthesis equation has no convergence problem: integral over a finite interval
    Let , if W=π
§5.1 DT FS to DT FT
Q1: Why?
Q2: Why?

## Slide 16: Fourier Transform of δ[n] and Complex Exponentials
x[n]=δ[n] 
§5.2 DT FT of Periodic Sequence
Q1: Why the coefficient 2π?
A: Check the inverse FT
Only one impulse in any consecutive interval of 2π

## Slide 17: Fourier Transform of Periodic Sequence
x[n] is a periodic sequence with period N
Fourier series of x[n]
§5.2 DT FT of Periodic Sequence

## Slide 18: Fourier Transform of Sinusoidal Sequence
+
§5.2 DT FT of Periodic Sequence
Q1: Aliasing?

## Slide 19: Fourier Transform of Periodic Impulse Train
, fundamental period N
  ???
Fourier series coefficients
§5.2 DT FT of Periodic Sequence
Choose [0, N-1] as sum interval

## Slide 20: Properties of DT Fourier Transform
Periodicity of DT Fourier Transform
Linearity of DT Fourier Transform
Time shifting
Frequency shifting
§5.3 DT FT Properties
Most important!

## Slide 21: Convolution Property
Recall: convolution integral
Fourier transform of y[n]
Convolution property of DT Fourier transform
§5.4 Convolution Property

## Slide 22: Response of Time-Shifting System
LTI system with impulse response
for input signal , output spectrum
=
From time shifting property
§5.4 Convolution Property

## Slide 23: Example 5.13: LTI System Response
LTI system with impulse response
input signal
output spectrum
if partial fraction expansion
output sequence
§5.4 Convolution Property
Q: What if ?

## Slide 24: Example 5.13: LTI System Response (cont’)
if , then
Using differentiation (frequency domain) property
Using time-shifting property
output sequence
§5.4 Convolution Property
Q: n=-1? Causality？

## Slide 25: Example 5.14: Ideal Bandstop Filter
§5.4 Convolution Property
=

## Slide 26: Example 5.14: Ideal Bandstop Filter (cont’)
§5.4 Convolution Property

## Slide 27: Multiplication Property
§5.5 Multiplication Property
=

## Slide 28: Linear Constant-Coefficient Difference Equation
N-th order Difference equation
Using time shifting property
Frequency response
§5.8 System Characterized by Difference Equations

## Slide 29: Example 5.18
LTI system with 1st order difference equation
Frequency response
Impulse response
§5.8 System Characterized by Difference Equations

## Slide 30: Example 5.19
LTI system with 2nd order difference equation
Frequency response
Partial fraction expansion
Impulse response
§5.8 System Characterized by Difference Equations

## Slide 31: DT Processing of CT Signals
C/D conversion: continuous-time to discrete-time conversion xd[n]=xc[nT]
D/C conversion: discrete-time to continuous-time conversion yc[nT] =yd[n]
§7.4 DT Processing of CT Signals

## Slide 32: C/D Conversion
impulse train
CT FT of
DT FT of
Since xd[n]=xc(nT)
=
§7.4 DT Processing of CT Signals
xd[n]=xc(nT)
=

## Slide 33: Spectrum of C/D Conversion
§7.4 DT Processing of CT Signals

## Slide 34: Impulse-Train Sampling of Discrete-Time Signals
§7.5 Sampling of DT Signals

## Slide 35: Impulse-Train Sampling of Discrete-Time Signals
In time domain,
In frequency domain,
DT FT of
Spectrum of
§7.5 Sampling of DT Signals

## Slide 36: Sampling of DT Signals without Aliasing
§7.5 Sampling of DT Signals

## Slide 37: Sampling of DT Signals with Aliasing
§7.5 Sampling of DT Signals

## Slide 38: Decimation
§7.5 Sampling of DT Signals
sampling
Decimation: operation of extracting every Nth sample

## Slide 39: Spectrum of Decimation
since =0 when n is not integer multiple of N,
§7.5 Sampling of DT Signals

## Slide 40: Spectrum of Decimation
§7.5 Sampling of DT Signals
Decimation is often called downsampling
If there is no aliasing in downsampling, then the original sequence is oversampled

## Slide 41: Interpolation
upsampling (reverse of decimation) + lowpass filter
§7.5 Sampling of DT Signals

## Slide 42: Summary
From DT FS to DT FT
FT of Periodic Sequence
DT Fourier Transform Properties
  Periodicity
  Convolution
Spectrum of Sampling, Decimation and Interpolation

## Slide 43: Duality Learned So Far
continuous-time Fourier transform: synthesis equation vs. analysis equation
discrete-time Fourier series: synthesis equation vs. analysis equation
§5.7 Duality

## Slide 44: No Duality between Synthesis Function and Analysis Function of DT FT
Summation vs. Integration: No duality in DT FT
No duality in CT FS
§5.7 Duality
Analysis equation
Synthesis equation
Synthesis equation
Analysis equation

## Slide 45: Duality between DT FT and CT FS
is a periodic signal, so it has FS expansion
§5.7 Duality
Synthesis equation
Analysis equation
Discrete-time
Fourier Transform
Continuous-time
Fourier Series

## Slide 46: Example 5.17
Example 5.17: Find the DT FT of
Consider CT signal g(t) with period of 2π
FS coefficients of g(t) is (Example 3.5)
Let , we have
The analysis equation
rename k as n and t as ω
replace –n by n,
Finally,
§5.7 Duality

## Slide 47: Basis for Discrete Fourier Transform (DFT)
Assume a signal with finite duration and limited band and
A periodic signal
FT of is given by
since ,
Q: Possible?

## Slide 48: Basis for Discrete Fourier Transform (DFT) (2)
Impulse sampling signal w/ sampling period Ts
The Fourier transform of

## Slide 49: Basis for Discrete Fourier Transform (DFT) (3)
Discrete-time signal , periodic and discrete in time domain, is represented by N= points in time domain
is periodic and discrete in frequency domain, is represented by N= points in frequency domain