## Slide 1
荷塘雨课堂
播放ppt
腾讯会议
双向语音/视频交流
2. 开启腾讯会议（请保持静音，一般关闭摄像头，发言前解除静音）
1. 开启荷塘雨课堂（请关闭音频输出，可以点名、白板、做题、弹幕等）
雨课堂可以看ppt，腾讯会议可以看现场板书，
建议分别用两个终端打开。

## Slide 2: Chapter 10 The z-Transform

## Slide 3: Outline
Definition of z-Transform
Region of Convergence of z-Transform
Inverse z-Transform
Geometric Evaluation of z-Transform
z-Transform Properties
LTI System Analysis Using z-Transform
System Block Diagram

## Slide 4: Recall: Discrete-time Fourier transform
Discrete-time Fourier transform pair
§10.1 Definition of z-Transform
Analysis equation
Synthesis equation

## Slide 5: Definition of z-Transform
Recall: LTI system with impulse response h[n]
  Output (sum convolution)
  System response to
  System function
If , is the discrete-time Fourier Transform of h[n]
Define z-transform for discrete-time signal x[n]
§10.1 Definition of z-Transform

## Slide 6: DT Fourier transform vs. z-Transform
Complex variable z in polar form
z-transform X(z) becomes
Then
Particularly, r=1
§10.1 Definition of z-Transform

## Slide 7: DT FT vs. z-Transform (cont’)
§10.1 Definition of z-Transform
Q: What in the s-plane is equivalent to the unit cycle in z-plane?

## Slide 8: Rational z-Transform
Rational z-transform: the z-transform is ratio of rational functions (polynomials)
Zeros: roots of numerator polynomial N(z)
Poles: roots of denominator polynomial D(z)
pole-zero plot in the z-plane
§10.1 Definition of z-Transform

## Slide 9: Example 10.1
x[n]=anu[n],
In the region of convergence (ROC) given by
or
§10.1 Definition of z-Transform
Q: What’s the condition that DT FT converges?
A: The ROC includes the unit cycle.
pole-zero plot

## Slide 10: Example 10.2
x[n]=-anu[-n-1]
In the region of convergence (ROC) given by
or
§10.1 Definition of z-Transform
Q: How to make DT FT converge?

## Slide 11: Example 10.3
, ROC1: , or
, ROC2: , or
ROC=ROC1∩ROC2:
§10.1 Definitionof z-Transform

## Slide 12: Example 10.4
-
ROC &
Actual ROC
§10.1 Definition of z-Transform
Q: The rational expression? Zero(s)?

## Slide 13: z-Transform ROC Property (1)
Convergence of X(z) is just the converge of DT FT of
Based on Dirichlet conditions, ROC of X(z) is given by the absolute summable condition:
 ROC is only related to r, but not ω
z-Transform ROC Property #1: ROC of X(z) consists of a ring in the z-plane centered about the origin
§10.2 ROC Properties of z-Transform

## Slide 14: z-Transform ROC Property (2)
z-Transform ROC Property #2: The ROC does not contain any poles
z-Transform ROC Property #3: If x[n] is of finite duration, then the ROC is the entire z-plane, except possibly z=0 and/or z=∞
  , ROC: z-plane including z=0 and z=∞
  , ROC: z-plane except z=0
  , ROC: z-plane except z= ∞
§10.2 ROC Properties of z-Transform

## Slide 15: z-Transform ROC Property (3)
Right-sided sequence: a sequence which is zero prior to some value of n, say, N1
z-Transform ROC Property #4: for a right-sided signal, if the circle is in the ROC, then the region outside this circle with finite values of z will also be in the ROC
  if N1 is positive, z=∞ is also in the ROC
  if N1 is negative, z=∞ is not in the ROC
  z-Transform ROC Property #5: for a left-sided signal, if the circle is in the ROC , then the region inside this circle with non-zero values of z will also be in the ROC
§10.2 ROC Properties of z-Transform
Q: How about z=0?

## Slide 16: z-Transform ROC of Sided Sequences
§10.2 ROC Properties of z-Transform
left-sided sequence
right-sided sequence
two-sided sequence

## Slide 17: Example 10.6
finite-duration sequence
z-transform
ROC Property #3  ROC is the entire z-plane
  including z=∞
  not including z=0
ROC Property #2  ROC does not include z=a?
§10.2 ROC Properties of z-Transform
Q: Why?
Q: Why?
Q: True or false?

## Slide 18: Example 10.7: Two-Sided Sequence
two-sided sequence: x[n]=b|n|, b>0
x[n]=bnu[n]+b-nu[-n-1]
, ROC1: , or
, ROC2: , or
if 0<b<1, , ROC:
if b>1, no z-transform
§10.2 ROC Properties of z-Transform
Q: Relationship between ROC an poles?

## Slide 19: z-Transform ROC Property (4)
z-Transform ROC Property #7: ROC of rational z-transform is bounded by poles or extends to ∞
z-Transform ROC Property #8: ROC of rational z-transform for left-sided sequence is the region inside the origin-centered circle with the radius equal to the smallest amplitude of poles, possibly including z=0.
  If anti-causal, then ROC includes z=0.
z-Transform ROC Property #9: ROC of rational z-transform for right-sided sequence
§10.2 ROC Properties of z-Transform
……?

## Slide 20: Inverse z-Transform
  When r is fixed, this integration corresponds to one traversal along the circle |z|=r
Inverse z-Transform
  contour integration
§10.3 Inverse z-Transform

## Slide 21: Example 10.8
ROC1: |z|>2,
ROC2: |z|<1/3 ,
ROC3: 1/3<|z|<2 ,
§10.3 Inverse z-Transform
Q2: z=0?
Q1: z=∞?

## Slide 22: Other Examples
X(z)=4z2+2+3z-1, 0<|z|<∞
x[n]=4δ[n+2]+ 2δ[n]+ 3δ[n-1]
Z{δ[n+n0]}=zn0
Taylor’s Series Expansion: when |x|<1
§10.3 Inverse z-Transform

## Slide 23: Geometric Evaluation of DT FT on Pole-Zero Plot
Discrete-time Fourier transform is the specific case of z-transform when (unit circle)
  Condition?
DT FT can be visualized from the pole-zero plot by checking the unit circle
Example #1:
  , ROC
  , if
  2 vectors:
    v1=ejω
    v2= ejω -a
§10.4 Geometric Evaluation of DT FT on Pole-Zero Plot
ROC includes the unit circle

## Slide 24: Geometric Evaluation of DT FT from Pole-Zero Plot (Example #1: a=0.5)
§10.4 Geometric Evaluation of DT FT on Pole-Zero Plot
a=0.5

## Slide 25: Geometric Evaluation of DT FT from Pole-Zero Plot (Example #1: a=0.95)
§10.4 Geometric Evaluation of DT FT on Pole-Zero Plot
a=0.95

## Slide 26: Geometric Evaluation of DT FT from Pole-Zero Plot (Example #2)
  If |r|<1, DT Fourier transform converges
poles and zeros
  a double zero at z=0
  2 conjugate poles
§10.4 Geometric Evaluation of DT FT on Pole-Zero Plot

## Slide 27: Geometric Evaluation of DT FT from Pole-Zero Plot (Example #2, Cont’)
poles and zeros
  a double zero at z=0
  2 conjugate poles
  3 vectors:
    v1=ejω
    v2= ejω -rejθ
    v3= ejω –re-jθ
DT Fourier transform
§10.4 Geometric Evaluation of DT FT on Pole-Zero Plot

## Slide 28: Geometric Evaluation of DT FT from Pole-Zero Plot (Example #2, r=0.8, θ=π/4)
§10.4 Geometric Evaluation of DT FT on Pole-Zero Plot
r=0.8
θ=π/4
Q: What’s the frequency corresponding to the peaks?

## Slide 29: z-Transform Properties - Linearity
Linearity:
§10.5 z-Transform Properties
Q1: ROC larger than ?
Q2: ROC = ?
A1: eg.
A2: no pole/zero cancellation

## Slide 30: z-Transform Properties – Time Shifting and Time Reversal
Time shifting:
, except possible addition/deletion of the origin/infinity
  n0>0, multiplication of may introduce additional pole(s) at 0 the origin z=0 is deleted from ROC
  n0<0 …..
Time reversal:
§10.5 z-Transform Properties

## Slide 31: z-Transform Properties – Time Expansion
Time expansion:
§10.5 z-Transform Properties

## Slide 32: z-Transform Properties – z-Domain Scaling
z-domain scaling:
A special case: ,
§10.5 z-Transform Properties

## Slide 33: z-Transform Properties – Conjugation
Conjugation:
If x[n] is real
  the magnitude-frequency response is even, the phase-frequency response is odd
§10.5 z-Transform Properties

## Slide 34: z-Transform Properties – Convolution
Convolution property
first-difference in time domain
  In time domain,
accumulation/summation in time domain
§10.5 z-Transform Properties
Q1: How to prove?
Q2: How?
Q3: ROC?
Q4: How?
Q5: ROC?

## Slide 35: z-Transform Properties – Differentiation in z-Domain
,
Differentiating both sides
§10.5 z-Transform Properties
Q1: ROC the same?
A1: No additional poles with differentiation

## Slide 36: Example 10.17 & 10.18
Example 10.17:
Example 10.19:
§10.5 z-Transform Properties

## Slide 37: Initial-Value Theorem
If x[n] is causal (x[n]=0 if n<0), then
Prove:
 for a causal sequence x[n] , is finite
 if is rational, then the order of the numerator polynomial cannot be higher than that of the denominator polynomial
Check Eg. 10.3:
§10.5 z-Transform Properties

## Slide 38: LTI System Characterized Using z-Transform
LTI system with impulse response h[n], input x[n]
Time domain response
System function/Transfer function
z-domain response
For z evaluated on the unit circle (), reduces to system frequency response
§10.7 LTI System Analysis Using z-Transform

## Slide 39: Causality
A LTI system is causal if and only if its impulse response h[n]=0 for all n<0 (Chapter 2)
A LTI system is causal if and only if the ROC of its system function is the exterior of a circle, including ∞
  right-sided sequence  ROC is the exterior of a circle (may or may not include ∞)
  h[n]=0 for all n<0  H(z) converges at ∞
A LTI system with rational system function H(z) is causal if and only if (i) the ROC of its system function is the exterior of a circle outside the outermost pole; and (ii) the order of the numerator polynomial is not higher than that of the denominator
  rational H(z)  ROC decided by poles
  initial-value theorem
§10.7 LTI System Analysis Using z-Transform

## Slide 40: Example 10.20, 10.21
Example 10.20,
Example 10.21,
§10.7 LTI System Analysis Using z-Transform

## Slide 41: Stability
A discrete-time LTI system is stable  its impulse response h[n] is absolutely summable (Chapter 2)
A discrete-time LTI system is stable  the Fourier transform of its impulse response h[n] converges
A discrete-time LTI system is stable  the ROC of its system function H(z) includes the unit circle |z|=1
A casual discrete-time LTI system is stable  all the poles of H(z) are inside the unit circle |z|=1
Examples:
  causal, unstable
  not causal, stable
  not causal, unstable
§10.7 LTI System Analysis Using z-Transform

## Slide 42: LTI Systems with Linear Constant-Coefficient Difference Equations
N-th order Difference equation
Use time shifting property
System function
§10.7 LTI System Analysis Using z-Transform

## Slide 43: Example 10.26
If system input is , then output is
If the system input is , then the output is
  is an eigen-function,
  , a=-9
, |z|>1/2
DE: y
§10.7 LTI System Analysis Using z-Transform
Q1: Why choose this ROC for H(z)?
A1: ROC of Y1(z) must include intersections of ROCs of X1(z) & H(z)

## Slide 44: Example 10.27
stable, causal system with impulse response h[n] and rational H(z), one pole at z=1/2, and a zero on the unit circle, all other poles and zeros are unknown
converges ?
for some ω ?
h[n] has finite duration ?
h[n] is real ?
g[n]=n[h[n]* h[n]] is the impulse response of a stable system ?
  h[n]=0 if n<0h[n]*h[n]=0 if n<0, g[n] is causal
  ,
  G(z) have the same pole locations as H(z) with rational H(z)
§10.7 LTI System Analysis Using z-Transform
A1: True. , ROC R/2
A2: True. At least one zero is ejω
A3: False. Finite duration means ROC=z-plane except 0/∞ vs. ROC can not include z=1/2(pole)
A4: Insufficient information. h[n] is real H(z）=H*(z*)

## Slide 45: Block Diagram of Feedback
§10.8 Block Diagram

## Slide 46: Block Diagram of 1st Order System (1)
§10.8 Block Diagram

## Slide 47: Block Diagram of 1st Order System (2)
()
let =, then
§10.8 Block Diagram

## Slide 48: Block Diagram of 2nd Order System (1)
§10.8 Block Diagram

## Slide 49: Block Diagram of 2nd Order System (2)
()
let =,
then
§10.8 Block Diagram

## Slide 50: Summary
From DT Fourier Transform to z-Transform
  z-plane vs. s-plane
  DT FT convergence
Region of Convergence of z-Transform
  relationship between ROC and poles
  sided sequence
  z=0, z=∞
Inverse z-Transform
  typical z-Transform pairs
z-Transform Properties
LTI System Analysis
  system function/transfer function
  causality
  stability
Block Diagram
Summary