## Slide 1
荷塘雨课堂
播放ppt
腾讯会议
双向语音/视频交流
2. 开启腾讯会议（请保持静音，一般关闭摄像头，发言前解除静音）
1. 开启荷塘雨课堂（请关闭音频输出，可以点名、白板、做题、弹幕等）
雨课堂可以看ppt，腾讯会议可以看现场板书，
建议分别用两个终端打开。

## Slide 2: Chapter 6 Time and Frequency Characterization of Signals and Systems

## Slide 3: Outline
Magnitude-Phase Representation of Frequency Response
Time/Frequency Domain Analysis of 1st Order and 2nd Order Continuous-Time Systems
Example of Time/Frequency Domain Analysis
Supplementary: Transfer Function of Typical Circuits

## Slide 4: Magnitude and Phase Response
Convolution property for LTI systems:
or
System gain (magnitude-frequency response):||
Phase shift (Phase-frequency response):
magnitude/phase distortions: unwanted change between the output and input
§6.2 Mag and Pha Frequency Response

## Slide 5: Linear Phase
Linear phase: the phase shift is linear (proportional to frequency, and the gain is constant (usually unit gain)
Frequency response of a linear phase CT system can be written as
Frequency response of a linear phase DT system can be written as
  : the slope of phase shift is integer
§6.2 Mag and Pha Frequency Response

## Slide 6: Linear Phase Shift = Time Shift
§6.2 Mag and Pha Frequency Response

## Slide 7: All-Pass System
All-pass system: the magnitude of the input spectrum is passed through unchanged by the system
CT all-pass system: the poles and zeros exist as pairs mirrored along the jω axis
§6.2 Mag and Pha Frequency Response

## Slide 8: Example 6.1
All-pass system
§6.2 Mag and Pha Frequency Response

## Slide 9: Group Delay
Delay for linear phase system:
  , , delay is
  , , delay is
Consider a narrowband signal centered at ω=ω0. With local linearization, the output phase shift in this narrow band is linear
is referred to as the group delay at ω0
Group delay at each frequency is the negative of the slope of the phase shift at that frequency
§6.2 Mag and Pha Frequency Response

## Slide 10: Principal vs. Unwrapped Phase
principal phase function : limit the values of phase between –π and +π
  sometimes limited to [0 2π) or other range of 2π
unwrapped phase function : appropriately adding or subtracting integer multiples of 2π from portions of the principal phase so that the phase function is continuous
group delay is computed on unwrapped phase function
§6.2 Mag and Pha Frequency Response

## Slide 11: Principal vs. Unwrapped Phase (cont’)
§6.2 Mag and Pha Frequency Response

## Slide 12: Additive Relationship
The relationship between the output signal FT phase and input signal FT phase and system transfer function phase is additive
  Cascaded system
Advantage to use the logarithmic scale for the magnitude of Fourier transform: the multiplication relationship is converted into the additive relationship
  Cascaded system
§6.2 Mag and Pha Frequency Response

## Slide 13: Unit of Decibel (dB)
System gain logarithmic system gain: A  20logA, with unit of decibel (dB)
  0 dB  gain=1
  gain of -20 dB  gain = 0.1 (attenuation of 20 dB)
  gain of 20 dB  gain = 10
dBV: logarithmic voltage referenced to 1 Volt
B Volt  20logB dBV
output voltage (dBV) = input voltage (dBV) + gain (dB)
output voltage = input voltage  system gain
Example: input voltage 2V, system gain 20, output voltage 40V  6 dBV + 26 dB = 32 dBV
logarithmic power gain: G  10logG, with unit of decibel (dB)
dBm: logarithmic power referenced to 1 mW
  P mW  10logP dBm
§6.2 Mag and Pha Frequency Response
Q: What’s the difference between voltage gain and power gain?

## Slide 14: Bode Plot
Bode plot: logarithmic amplitude and phase vs. frequency, namely, and versus (usually in continuous-time case)
  the amplitude axis is logarithmic
  the frequency axis is logarithmic for continuous-time system:
  the frequency axis is linear for discrete-time system, but limited to a range of 2π:
Usually we only show >0 for the bode plot
  if h(t) is real, then is even, and is odd, we can easily plot and for <0
§6.2 Mag and Pha Frequency Response
Q: Is the axis label in the phase-frequency plots correct in Fig. 6.8 & 6.9?
Q: Why?

## Slide 15: Typical Bode Diagram
§6.2 Mag and Pha Frequency Response
Bode Plot
Frequency Response

## Slide 16: First-Order Continuous-Time System
Here we only consider LTI systems characterized by linear constant-coefficient differential equations
First-order CT system differential equation
System function / transfer function
, with one pole
Frequency response
§6.5 1st and 2nd Order CT Systems
time constant

## Slide 17: System Response of First-Order Continuous-Time System
Impulse response
Step response
How to find s(t) using the inverse FT?
§6.5 1st and 2nd Order CT Systems

## Slide 18: System Response of First-Order Continuous-Time System (Cont’)
§6.5 1st and 2nd Order CT Systems
2τ
τ/1
τ/1
τ/1
0
1/τ
h(t)
s(t)
t
t
4τ
5τ
6τ
3τ
τ
2τ
τ/1
τ/1
0
4τ
5τ
6τ
3τ
τ
1/eτ
1-1/e

## Slide 19: Asymptotic Approximation of Magnitude-Frequency Response of 1st Order System
Magnitude-frequency response
Approximation #1:
Approximation #2:
,
break frequency / cutoff frequency / corner frequency: the frequency point for which the magnitude is -3 dB lower than the nominal passband value (half-power point)
break frequency of first order system:
or
§6.5 1st and 2nd Order CT Systems
-20 dB per decade

## Slide 20: Asymptotic Approximation of Magnitude-Frequency Response of 1st Order System (cont’)
§6.5 1st and 2nd Order CT Systems
1/τ
10/τ
100/τ
0.1/τ
0
|H(jω)|
(dB)
-20
-40
-60
3dB
— magnitude response
---Asymptotic Approximation
ω
ωc

## Slide 21: Asymptotic Approximation of Phase-Frequency Response of 1st Order System
Phase-frequency response
Asymptotic approximation
at the break frequency , =
§6.5 1st and 2nd Order CT Systems
-π/2 phase shift for each left half-plane pole
Q: Valid for complex pole?

## Slide 22: Asymptotic Approximation of Phase-Frequency Response of 1st Order System (cont’)
§6.5 1st and 2nd Order CT Systems
1/τ
10/τ
100/τ
0.1/τ
ω
0
-π/4
-π/2
— frequency response
---Asymptotic Approximation

## Slide 23: Second-Order CT Systems
Linear constant-coefficient differential equation of second-order system
System function
frequency response
frequency can be normalized to
-- damping ratio, -- undamped natural frequency
  , system is underdamped, conjugate pole pair on the left half-plane, oscillation in impulse response
  , system is overdamped, two negative poles, no oscillation in impulse response
  , system is critically damped
  Quality factor:
§6.5 1st and 2nd Order CT Systems
Q1: Form of h(t)?
Q2: Form of h(t)?

## Slide 24: Asymptotic Approximation of Magnitude-Frequency Response of 2nd Order System
Magnitude-frequency response
Approximation #1:
Approximation #2:
§6.5 1st and 2nd Order CT Systems
-40 dB per decade for 2 poles!

## Slide 25: Asymptotic Approximation of Magnitude-Frequency Response of 2nd Order System (cont’)
§6.5 1st and 2nd Order CT Systems
0
|H(jω)|
(dB)
-20
-80
6dB
Asymptotic Approximation
ω
-60
-40
, no peak
Q: What’s the optimal ζ?
The peak sharpness is decided by , or the quality factor

## Slide 26: Asymptotic Approximation of Phase-Frequency Response of 2nd Order System
§6.5 1st and 2nd Order CT Systems
ω
0
-π/2
-π
Asymptotic Approximation
-π phase shift for two left half-plane poles

## Slide 27: Impulse Response of Second-Order CT System
§6.5 1st and 2nd Order CT Systems
Q: What’s the optimal ζ?

## Slide 28: Step Response of Second-Order CT System
§6.5 1st and 2nd Order CT Systems
Q: What’s the optimal ζ?

## Slide 29: Bode Plots of Basic Rational Frequency Responses
§6.5 1st and 2nd Order CT Systems

## Slide 30: Example 6.5 -- Part A
§6.5 1st and 2nd Order CT Systems
ω
|H(jω)|
(dB)

## Slide 31: Example 6.5 – Part B
§6.5 1st and 2nd Order CT Systems
ω
0
-π/2
π/2

## Slide 32: Example 6.5: Bode Plot vs. Asymptotic Approximation
§6.5 1st and 2nd Order CT Systems

## Slide 33: Automobile Suspension System
variation of x(t) represents roughness of road surface
Requirement #1: filter out rapid variations  lowpass filter
Requirement #2: no sharp division between frequencies to be passed or rejected  gradual transition passband and stopband
Requirement #3: no oscillatory response when encountering a bump or curb  no ringing in impulse response or step response
§6.7 Examples of Time/Frequency Domain Analysis

## Slide 34: Equations of Automobile Suspension System
Differential equation:
, ,
Frequency response:
Let ,
§6.7 Examples of Time/Frequency Domain Analysis

## Slide 35: Magnitude-Frequency Response of Automobile Suspension System
§6.7 Examples of Time/Frequency Domain Analysis
ω
0
|H(jω)|
(dB)
-20
-40
20
More closer to TF of a single-pole system

## Slide 36: Step Response of Automobile Suspension System
§6.7 Examples of Time/Frequency Domain Analysis
Conflict requirement:
Lowpass filtering  small ωn
Rapid response  large ωn
Trade-off of ζ
Too small ζ  ringing (uncomfortable)
Large ζ helps to speeding up settling
(Figure 6.34 is not correct)

## Slide 37: s-Domain Modeling of RLC
resistor:
apply Laplace transform to both sides
Impedance
inductor:
apply Laplace transform to both sides
Impedance
capacitor:
apply Laplace transform to both sides
Impedance
S: Transfer Function of Typical Circuits

## Slide 38: System Function of RLC System
S: Transfer Function of Typical Circuits
X(s)
sL
1/sC
Y(s)

## Slide 39: Modeling of Operational Amplifier
Transfer function of operational amplifier:
virtually open: input impedance very high  no current into Vi+/Vi-
virtually short: gain is huge, and Vi+-Vi-≈0
S: Transfer Function of Typical Circuits

## Slide 40: Active RC Filter (Integrator)
Only consider that the amplifier has a constant gain A0
=--
Only consider that the amplifier has a constant gain A0
If directly using “virtually short”, , …….
S: Transfer Function of Typical Circuits
Q: What if ?

## Slide 41: Active RC Filter (Lowpass)
=-
S: Transfer Function of Typical Circuits

## Slide 42: Active RC Filter (Highpass)
=-
S: Transfer Function of Typical Circuits

## Slide 43: Active RC Filter (Highpass)
Transfer Function?
S: Transfer Function of Typical Circuits

## Slide 44: Active RC Filter (Lowpass with Finite Attenuation)
Transfer Function?
S: Transfer Function of Typical Circuits

## Slide 45: Summary
Definition of Bode plot
Bode plots of 1st order and 2nd order system
Transfer functions of simple circuits
  s-domain modeling
  transfer function analysis