## Slide 1
荷塘雨课堂
播放ppt
腾讯会议
双向语音/视频交流
2. 开启腾讯会议（请保持静音，一般关闭摄像头，发言前解除静音）
1. 开启荷塘雨课堂（请关闭音频输出，可以点名、白板、做题、弹幕等）
雨课堂可以看ppt，腾讯会议可以看现场板书，
建议分别用两个终端打开。

## Slide 2: Chapter 2 Brief: Convolution
#1 Linear
#2 Time invariant
#3 (Sampling) property of unit impulse

## Slide 3: Supplementary Material 1 Time-Domain Response
2020-09-30

## Slide 4: Outline
Differential Equations
Homogeneous Solution and Particular Solution
Initial Conditions
Zero-Input and Zero-State Responses

## Slide 5: System Description Using Differential Equations
Constitutive definition of capacitors
Kirchhoff’s Voltage Law (KVL)
Reorder
§S1.1 Differential Equations

## Slide 6: System Description Using Differential Equations
Total force on the vehicle
Newton’s Second Law of Motion
Combine them
§S1.1 Differential Equations

## Slide 7: System Description Using Differential Equations
input is(t), output v(t)
KCL
§S1.1 Differential Equations

## Slide 8: System Description Using Differential Equations
§S1.1 Differential Equations
MEMS accelerometer (http://www.memx.com）
Equivalent Model (https://wiki.metropolia.fi)
spring stiffness coefficient k, damping factor f, mass m, external force Fs(t), velocity of proof mass v(t)

## Slide 9: Homogeneous Solution and Particular Solution
Linear constant-coefficient differential equation
Complete solution y(t)=yp(t)+yh(t)
yh(t) homogeneous solution, the solution when the right part of the differential equation is 0 (different from the zero-input response!)  natural response
yp(t) particular solution, the solution dependent on the excitation function forced response
§S1.2 Homogeneous Solution and Particular Solution

## Slide 10: Homogeneous Solution
To find yh(t), solve the characteristic equation
If no multiple roots
If multiple roots exist
the corresponding part in yh(t)
Eg. Find yh(t) for
§S1.2 Homogeneous Solution and Particular Solution
How to find Ak?

## Slide 11: Particular Solution
Step #1: excitation function  particular solution (based on experience)
E (constant) B (constant)
tp  Bptp+Bp-1tp-1+…+B1t+B0
eat  Beat
cos(ωt) or sin(ωt)  B1cos(ωt) + B2sin (ωt)
tpeatcos(ωt) or tpeatsin(ωt)
 (Bptp+Bp-1tp-1+…+B1t+B0) eatcos(ωt)
+ (Dptp+Dp-1tp-1+…+D1t+D0) eatsin (ωt)
……
Step #2: Find the unknown coefficients: Bk, Dk
§S1.2 Homogeneous Solution and Particular Solution
How?

## Slide 12: Examples to Find Particular Solution
(1) x(t)=t2
the right side =t2+2t, try y(t)=B2t2+B1t+B0
(2) x(t)=et
Try y(t)=Bet, Bet + 2Bet + 3Bet =et+et,  B=1/3
§S1.2 Homogeneous Solution and Particular Solution

## Slide 13: How to Find Coefficients {Ak}
Complete solution
N auxiliary conditions are required to find N coefficients {Ak} (k=N, N-1, …, 1)
Typical auxiliary conditions: for any time t0, {y(t0), dy(t0)/dt, d2y(t0)/dt2, …, dN-1y(t0)/dtN-1}
Usually, let t0=0 since the excitation is effective for 0≤t<∞
§S1.2 Homogeneous Solution and Particular Solution
Vandermonde Matrix

## Slide 14: Steps to Find Complete Solution
Step #1: Write the differential equation
Step #2: Find the homogeneous solution yh(t) ({Ak} unknown)
Step #3: Find the particular solution yp(t)
Step #4: Decide the auxiliary conditions (initial conditions
Step #5: Find {Ak} for yh(t)
Step #5: Complete solution= yh(t)+ yp(t)
§S1.2 Homogeneous Solution and Particular Solution

## Slide 15: Initial Conditions (初始条件)
Initial states: y(t0), y’(t0), y’’(t0), …
Usually we choose t0=0,  y(0), y’(0), y’’(0), …
Pre-initial states: y(0-), y’(0-), y’’(0-), … (起始状态)
Post-initial states: y(0+), y’(0+), y’’(0+), … (初始状态)
Use the post-initial states as the initial conditions to find {Ak} , since the input is effective only after t0
  do not necessarily use the initial states as the initial conditions
Initial rest condition: y(t)=0 for t<0
y(0-)=0, y’(0-)=0, y’’(0-)=0, …
§S1.3 Initial Conditions

## Slide 16: Example: Initial Conditions with Initial Rest
input: vS(t)=sin(2t)u(t)
Homogenous solution
Particular solution: try
Complete solution:
Initial Rest:
§S1.3 Initial Conditions
Anything Wrong?

## Slide 17: Example: Initial Conditions with Initial Rest (cont’)
input: vS(t)=sin(2t)u(t)
Complete solution:
Initial Rest:
Actually, initial rest only leads to v(0-)=0, v’(0-)=0, while it does NOT imply v(0+)=0, v’(0+)=0
We can analyze v(0+)=0, v’(0+)=0
  voltage across C2 cannot change instantly v(0+)= v(0-)=0
  vC1(0+)=0  iR2(0+)= iC2(0+)=0 vC2’(0+)=0
§S1.3 Initial Conditions

## Slide 18: Zero-Input Response and Zero-State Response
Does the homogeneous solution have nothing to do with the input?
No! The homogeneous solution can be divided into two parts: the output due to the pre-initial states, the output due to the input (excitation)
§S1.4 Zero-Input Response and Zero-State Response

## Slide 19: Zero-Input Response and Zero-State Response
Zero-Input Response: system response determined by the pre-initial states. It has nothing to do with the input/excitation
Zero-State Response: system response with all-zero pre-initial states. It is determined only by the external excitation
  The previous examples all consider the zero-state response
§S1.4 Zero-Input Response and Zero-State Response

## Slide 20: Example with non-zero pre-initial states
LTI system
Homogeneous solution
Particular solution
Complete solution
Zero-input response:
Zero-state response:
§S1.4 Zero-Input Response and Zero-State Response

## Slide 21: Impulse Response: Find Initial States by Matching the Singularity Equations (1)
Principle: the coefficients of singularity functions must be the same on the two sides of DE
Example: y’ (t)+3 y(t)= 3x’ (t) x(t)=δ(t) initial rest
t>0+, only homogeneous solution y’ (t)=Ae-3t
There is 3δ’ (t) on the right side  there must be the term 3δ’ (t) in y’ (t)  there must be the term 3δ(t) in y(t)
there is no δ(t) on the right side  there must be the term -9δ(t) in y’ (t)  there is the term -9Δu(t) in y(t) (Δu(t) represents a jump function, not just a step)
 y(0+)=y(0-)-9=-9  A=-9, y(t)= -9e-3t (t>0+)
The full impulse response is h(t)=3δ(t) -9e-3tu(t) (-∞<t< ∞)
§S1.3 Initial Conditions

## Slide 22: Impulse Response: Find Initial States by Matching the Singularity Equations (2)
Example: iS(t)= δ(t) + initial rest
Particular response yp(t)=0, since excitation=0 for t>0
Only homogeneous solution
Initial conditions:
  iL’’(t) must contain δ(t)/LC
   iL’(t) must contain a step with the magnitude equals to 1/LC  iL’(0+)=iL’(0-)+1/LC=1/LC
   iL’(0) is bounded  iL(t) is continuous from t=0- to t=0+  iL (0+)= iL (0-)=0
§S1.3 Initial Conditions
Q1: Output independent of input?
Q2: Physical Meaning?
A: Do not consider physical meaning here

## Slide 23: Linear Constant-Coefficient Difference Equation
Nth-order
y[n]=yp[n]+yh[n]
yp[n] particular solution, yh[n] homogeneous solution
How to find yh[n]
  Solve the characteristic equation:
  If no multiple roots,
  If multiple roots exist, the corresponding part in yh[n]
  Eg. 2.15
§2.4 Differential and Difference Equations

## Slide 24: Summary
The presented content in this document only focuses on t > 0+. It does not effectively give a comprehensive solution for -∞ <t < ∞
Natural response + Forced response
  Natural response: homogeneous
  Forced response: particular
Zero-input response + Zero-state response
  Zero-input response: homogeneous
  Zero-state response: homogeneous + particular
S1. Time-Domain Response