## Slide 1
荷塘雨课堂
播放ppt
腾讯会议
双向语音/视频交流
2. 开启腾讯会议（请保持静音，一般关闭摄像头，发言前解除静音）
1. 开启荷塘雨课堂（请关闭音频输出，可以点名、白板、做题、弹幕等）
雨课堂可以看ppt，腾讯会议可以看现场板书，
建议分别用两个终端打开。

## Slide 2: Chapter 1 Signals and Systems

## Slide 3: Outline
Continuous-Time and Discrete-Time Signals
Transformation of the Independent Variables
Exponential and Sinusoidal Signals
Unit Impulse and Unit Step Functions
Continuous-Time and Discrete-Time Systems
Basic System Properties

## Slide 4: §1.1 Continuous-Time & Discrete-Time Signals
Mathematical representation of signals: function of one or more independent variables
  Number of independent variables
    We focus on the single independent variables case
  Generally refer to the independent variable as time, but actually may not be time
Signal classification
  Deterministic signal vs. random signal
  Continuous-time vs. discrete-time signal
Continuous-time signal: x(t)
Discrete-time signal: x[n] (Sequence)
§1.1 Continuous-Time & Discrete-Time Signals

## Slide 5: Discrete-Time Signals
Originally discrete-time signals
  Stock market index
  Monthly bank account balance
Discretization of continuous-time signals
  Speech signals
  Image signals
  …..
§1.1 Continuous-Time & Discrete-Time Signals

## Slide 6: Signal Energy and Power
Recall: energy & power definition for a resistor R
  Instantaneous power
  Energy over the time interval t1 < t < t2
  Average power for t1 < t < t2
  All with the corresponding dimensions
§1.1 Continuous-Time & Discrete-Time Signals

## Slide 7: Signal Energy and Power
Continuous-time signal x(t)
  Signal energy for t1 < t < t2
  Signal average power for t1 < t < t2
  Signal energy for −∞ < t < +∞
  Signal average power for −∞ < t < +∞
§1.1 Continuous-Time & Discrete-Time Signals
Q: Dimension?

## Slide 8: Signal Energy and Power
Discrete-time signal x[n]
  Signal energy for n1 ≤ n ≤ n2
  Signal average power for n1 ≤ n ≤ n2
  Signal energy for −∞ < n < +∞
  Signal average power for −∞ < n < +∞
§1.1 Continuous-Time & Discrete-Time Signals

## Slide 9: 3 classes of signals
1. Finite total energy E∞< ∞ => zero average power P∞=0
e.g.
2. Finite average power P∞ < ∞, infinite total energy E∞=∞
3. Infinite average power P∞=∞
e.g.?
§1.1 Continuous-Time & Discrete-Time Signals
e.g. ?
x[n]=1, x(t)=cosωt

## Slide 10: §1.2 Transformations of Independent Variables
Time shift: x(t)  x(t-t0), x[n]  x[n-n0]
  Left shift? Right shift?
Time reversal: x(t)  x(-t), x[n]  x[-n]
Time scaling: x(t)  x(αt), x[n]  x[αn] (?)
  │α│>1 compress
  │α│<1 stretch
  Q: How to fast forward a music player?
General form: x(t)  x(αt+β), x[n]  x[αn+k](?)
Example 1.1: x(t+1), x(-t+1), x(1.5t), x(1.5t+1)

## Slide 11: Periodic Signals
Periodic Signals:
  x(t)= x(t+T)
  x[n]= x[n+N]
fundamental period: the smallest positive value of T/N, denoted as T0/N0
Q: what is the period of a constant signal?
§1.2 Transformations of Independent Variables
  Yes, but NO fundamental period

## Slide 12: Even and Odd Signals
Even signal: x(-t)=x(t), x[-n]=x[n]
Odd signal: x(-t)=-x(t), x[-n]=-x[n]
  x(0)=0, x[0]=0
any signal can be written as the sum of an even signal and an odd signal
  even part:
  odd part:
§1.2 Transformations of Independent Variables

## Slide 13: §1.3 Exponential and Sinusoidal Signals
Complex exponential signal:
Real exponential signal: C and a are all real
  a>0, growing exponential
  a<0, decaying exponential
Periodic complex exponential: C is real, a is purely imaginary
  Fundamental period
  Energy and average power over one period
§1.3 Exponential and Sinusoidal Signals

## Slide 14: Exponential and Sinusoidal Signals (cont’)
Sinusoidal signal:
harmonically related complex exponentials: sets of periodic exponentials with a common period T0
kth harmonic ϕk(t), fundamental frequency │k│ ω0, fundamental period T0/ │k│
§1.3 Exponential and Sinusoidal Signals

## Slide 15: Continuous-time exponential vs. discrete-time exponential
vs.
distinct signals for distinct ω0 vs. identical signals for ω0 values separated by 2π
always periodic vs. periodic only if ω0 = 2πm/N
fundamental frequency ω0 vs. fundamental frequency ω0/m
§1.3 Exponential and Sinusoidal Signals

## Slide 16: §1.4 Unit Impulse & Unit Step Functions
Discrete-time unit impulse
Discrete-time unit step
§1.4 Unit Impulse & Unit Step Functions
(unit sample)

## Slide 17: Relationship between unit impulse and unit step
δ[n] is the first difference of u[n]
u[n] is the running sum of δ[n]
u[n] is a superposition of the delayed unit impulses
§1.4 Unit Impulse & Unit Step Functions

## Slide 18: Continuous-Time Unit Step
Continuous-time unit step
No definition for t=0
  some textbooks let u[t]=0.5 @ t=0
e.g.
§1.4 Unit Impulse & Unit Step Functions

## Slide 19: Continuous-Time Unit Impulse
u(t) is the running integral of unit impulse δ(t)
δ(t) is the first derivative of u(t)
But how? u(t) is not differentiable at t=0 !
Dirac Definition of unit impulse
§1.4 Unit Impulse & Unit Step Functions
Very short time
Very large value

## Slide 20: Definition of Unit Impulse
§1.4 Unit Impulse & Unit Step Functions
δ(t) is the idealization of a pulse which is “short enough”
Another definition
Meet Dirac Definition?

## Slide 21: Sampling Property of Unit Impulse
In real circuit, only short pulses are available for sampling. If the pulse is “short enough”
§1.4 Unit Impulse & Unit Step Functions
Q1: What is “short enough”? See Chapter 7
Q2: δ(2t)=δ(t)? u(2t)=u(t)?

## Slide 22: §1.5 Systems
A system is a process in which input signals are transformed, resulting in other signals as outputs.
continuous-time systems vs. discrete-time systems
§1.5 Systems

## Slide 23: Examples of continuous-time systems
A wide range of physical systems can be modeled within the class of systems that will be covered in this course
§1.5 Systems

## Slide 24: Examples of discrete-time systems
month to month bank account balance
Discrete-time representation of the automobile system
§1.5 Systems
A wide range of physical systems can be modeled within the class of systems that will be covered in this course

## Slide 25: Interconnections of Systems
Series/cascade interconnection
Parallel interconnection
Feedback interconnection
§1.5 Systems

## Slide 26: §1.6 Basic System Properties
System with/without memory
A system is memoryless if the output at a given time is dependent on the input at the same time.
  e.g., a resistor is memoryless
Systems with memory
  a capacitor is a continuous-time system with memory
  an accumulator/summer is a discrete-time system with memory:
§1.6 Basic System Properties
Memristor?

## Slide 27: Invertibility
A system is invertible if distinct inputs leads to distinct outputs.
  A system is invertible, then an inverse system exists
e.g., w(t)=y(t)/2 is the inverse system of y(t)=2x(t)
Q: what is the inverse system of ?
Application example: lossless compression
§1.6 Basic System Properties

## Slide 28: Causality
A system is causal/nonanticipative if the output at any time is not dependent on the input after that time
Non-causality is common in processing previously recorded signals, such as speech, video…
Q1: is y[n]=x[-n] causal?
Q2: is y(t)=x(t+1) causal?
§1.6 Basic System Properties

## Slide 29: Time Invariance
A system is time invariant if a time shift in the input results in an identical time shift in the output.
Intuitively, the input-output relationship does not changes with time.
Example 1.14, is y(t)=sin[x(t)] time invariant?
Example 1.15, is y[n]=nx[n] time invariant?
§1.6 Basic System Properties

## Slide 30: Linearity
A linear system is a system with the superposition property.
Superposition property = additivity property + scaling/homogeneity property
Example 1.20: is y[n]=2x[n]+3 linear?
Example 1.17: is y(t)=tx(t) linear?
§1.6 Basic System Properties

## Slide 31: Summary
Time-domain representation of signals
  Transformation
  Period signals
  Unit step and unit impulse
Time-domain representation of systems
We will focus on linear, time-invariant (LTI) systems in the remaining part of this course