## Slide 1
荷塘雨课堂
播放ppt
腾讯会议
双向语音/视频交流
2. 开启腾讯会议（请保持静音，一般关闭摄像头，发言前解除静音）
1. 开启荷塘雨课堂（请关闭音频输出，可以点名、白板、做题、弹幕等）
雨课堂可以看ppt，腾讯会议可以看现场板书，
建议分别用两个终端打开。

## Slide 2: Chapter 9 The Laplace Transform

## Slide 3: Limitation of Fourier Transform
Recall: Fourier Transform
Convergence--Dirichlet Condition #1: absolutely integrable
What if x(t) and/or h(t) is not absolutely integrable? Unstable!
 The Fourier transform can not be used for unstable system/signals
The Laplace transform can be used to analyze unstable systems/signals
Not just to handle unstable systems/signals
  The Laplace transform is more powerful in many ways
§9.1 Laplace Transform

## Slide 4: Outline
Laplace Transform
Region of Convergence for Laplace Transform
Inverse Laplace Transform
Laplace Transform Properties
LTI System Analysis Using Laplace Transform
System Block Diagram

## Slide 5: Laplace Transform
Recall: LTI system response to eigen-function
H(s) is the Laplace transform of h(t)
If s is purely imaginary, then H(s) is the Fourier Transform
Laplace transform:
Laplace transform operator
§9.1 Laplace Transform

## Slide 6: Relationship between Fourier Transform and Laplace Transform
Fourier transform is a special case of Laplace transform when s is purely imaginary
Laplace transform of x(t) is the Fourier transform of x(t)e-σt
§9.1 Laplace Transform
This Fourier transform may NOT converge!
Q: Is the relationship really that simple?

## Slide 7: Example 9.1
signal x(t)=e-atu(t)
Fourier transform converges only when a>0
Laplace transform
When
§9.1 Laplace Transform

## Slide 8: Example 9.2
signal x(t)=-e-atu(-t)
Fourier transform converges only when a<0
Laplace transform
When
§9.1 Laplace Transform

## Slide 9: Region of Convergence (ROC)
Two different signals, the same expression for Laplace transform
Region of Convergence (ROC): the range of values of s for which the Laplace integral converges
§9.1 Laplace Transform
?
Laplace transform = integral + ROC
Q: Laplace transform of δ(t)? ROC?

## Slide 10: ROC on the s-plane
§9.1 Laplace Transform
Example 9.2
Example 9.1

## Slide 11: Example of ROC (Example 9.3)
§9.1 Laplace Transform

## Slide 12: ROC of Complex Exponential
ROC is only dependent on the real part (a), but not on the imaginary part (jb)
§9.1 Laplace Transform

## Slide 13: Poles/Zeros of Rational Laplace Transform
Rational Laplace transform: ratio of rational functions (polynomials)
X(s) is rational if x(t) is a linear combination of real/complex exponentials
Zeros: roots of numerator polynomial N(s)
Poles: roots of denominator polynomial D(s)
pole-zero plot: representation of X(s) through its poles and zeros in the s-plane
Example:
§9.1 Laplace Transform

## Slide 14: Pole-Zero Plot
§9.1 Laplace Transform
Q: How to define pole/zero of infinity?

## Slide 15: Laplace Transform Convergence vs. Fourier Transform Convergence
If the Laplace transform ROC does not contain the jω-axis, then the Fourier transform does not converge
§9.1 Laplace Transform

## Slide 16: Properties of Laplace Transform ROC
Property #2: The ROC does not contain the poles
Question: How to find X(s) for the poles? Use L’hospital’s Rule
Property #3: If x(t) is of finite duration and absolutely integrable, then the ROC is the s-plane
Question: example?
δ(t)
§9.2 ROC for Laplace Transform

## Slide 17: Sided Signals
Right-sided signal: There exists a finite time T1, x(t)=0 for t<T1
Property #4: Right-sided signal has an ROC (if exists) containing a right-sided plane
  right-sided plane is not the half-plane right to jω axis
Left-sided signals: There exists a finite time T1, x(t)=0 for t>T1
Property #5: Left-sided signal has an ROC (if exists) containing a left-sided plane
Property #6: The ROC of a two-sided signal (if exists) contains a strip in parallel with the jω axis
§9.2 ROC for Laplace Transform

## Slide 18: Properties of Laplace Transform ROC
Property #7: Rational Laplace transform X(s), ROC is bounded by poles or extended to infinity
  entire s-plane
  left-sided plane for left-side signals
  right-sided plane for right-side signals
  a single strip for two-sided signals
§9.2 ROC for Laplace Transform

## Slide 19: Inverse Laplace Transform
Recall: Fourier transform pair
Laplace transform based on Fourier transform
Inverse FT
Change the integration variable to s
Inverse Laplace transform
§9.3 Inverse Laplace Transform

## Slide 20: How to Solve Inverse Laplace Transform
Formal inverse Laplace transform requires contour integration in the complex plane
For rational Laplace transform, use partial-fraction expansion
If ROC is to the right of s=-ai
If ROC is to the left of s=-ai
§9.3 Inverse Laplace Transform
Q: pole inside ROC?
A: See ROC property #8

## Slide 21: Examples of Inverse Laplace Transform
§9.3 Inverse Laplace Transform

## Slide 22: Linearity of Laplace Transform
§9.5 Laplace Transform Properties
Discussion:
If the intersection of R1 and R2 is empty, no Laplace transform
x1(t)=x2(t), and a=-b, then ROC becomes the entire s-plane

## Slide 23: ROC Extension by Pole-Zero Cancellation
§9.5 Laplace Transform Properties

## Slide 24: Time Shifting of Laplace Transform
§9.5 Laplace Transform Properties
Discussion: Laplace transform exists does not necessarily mean that X(s) is bounded

## Slide 25: Time Scaling of Laplace Transform
Compression in the time domain  Expansion in the s-domain
Time reversal
§9.5 Laplace Transform Properties
Q: Is Eq. (9.90) correct?

## Slide 26: s-Domain Shifting
zero zz+s0, pole pp+s0
A special case: s0=jω0
frequency modulation  shift in the s-plane along the jω axis
§9.5 Laplace Transform Properties
, with ROC R1=R

## Slide 27: Conjugation
A useful observation: if x(t) is real, then any complex pole/zero must exist as a conjugate pair, i.e., if s0 is complex and a pole/zero, then s0* is also a pole/zero
§9.5 Laplace Transform Properties

## Slide 28: Convolution Property of Laplace Transform
§9.5 Laplace Transform Properties
Discussion: the ROC of convolution might be larger than R1∩R2
Pole-Zero Cancellation
Q: Any example?

## Slide 29: Differentiation in Time Domain
Recall: Inverse Laplace transform
Differentiate both sides w.r.t t
If X(s) has a first-order pole at s=0, then ROC of sX(s) may be larger than ROC of X(s)
Example: x(t)=u(t), X(s)=1/s, ROC=right half plane
§9.5 Laplace Transform Properties

## Slide 30: Differentiation in s-Domain
Recall Laplace transform
Differentiate both sides w.r.t s
§9.5 Laplace Transform Properties
Q: Any problem with the new ROC?
A: The new ROC is correct if X(s) is rational. We can expand X(s) as the combination of first-order fractions.

## Slide 31: Differentiation in s-Domain--Examples
§9.5 Laplace Transform Properties
Partial-fraction expansion

## Slide 32: Integration in Time Domain
Integration convolution
Convolution property +
§9.5 Laplace Transform Properties

## Slide 33: Initial-Value and Final-Value Theorems
Assumption: x(t)=0 for t<0, and x(t) contains no impulses or higher order singularities
Initial-value theorem
Final-value theorem
Check Example 9.3
§9.5 Laplace Transform Properties
Homework: Prove them.

## Slide 34: Laplace Transform Pairs
Usually a signal is right-sided, and the corresponding ROC is the right-sided plane.
 Usually we take the right-sided signals and right-sided plane ROC as the default
§9.6 Laplace Transform Pairs

## Slide 35: System Function / Transfer Function
Recall convolution integral: LTI system with the impulse response: h(t), the time-domain response to any signal x(t)
Based on convolution property of L-transform
H(s) is called the system function or transfer function
§9.7 LTI System Analysis Using Laplace Transform

## Slide 36: System Causality
Recall: A system is causal if the output at any time is not dependent on the input after that time
A LTI system is causal if and only if h(t)=0 for t<0
Statement #1: If a LTI system is causal, the ROC of the system function is a right-sided plane (sufficient, not necessary)
Statement #2: If a LTI system is causal with a rational H(s), causality is equivalent to that the ROC of the system function is a right-sided plane to the right of the rightmost pole (sufficient and necessary)
§9.7 LTI System Analysis Using Laplace Transform
Q: How to prove? (convolution integral)

## Slide 37: System Causality--Examples
1st example of Statement #2 (rational, causal, ROC is a right-sided plane)
2nd example of Statement #2 (rational, not causal, ROC is not a right-sided plane)
An example that shows Statement #1 is sufficient but not necessary (not rational, ROC is a right-sided plane, not causal)
§9.7 LTI System Analysis Using Laplace Transform
Q1: pole(s)?
Q2: How to do Laplace transform?
(Time Shifting)

## Slide 38: System Stability
Stability: (Chapter 1) A system is stable if any bounded input produces a bounded output.
A system is stable if and only if h(t) is absolutely integrable
Statement #1: A LTI system is stable if and only if the ROC of H(s) includes the entire jω axis
  If the 2nd and 3rd conditions of Dirichlet Conditions are satisfied, then absolutely integrable  Fourier transform convergence
Statement #2: A causal system with rational H(s) is stable if and only if all poles of H(s) are left-half-plane poles
  causality  ROC is to the right of rightmost poles
§9.7 LTI System Analysis Using Laplace Transform
Q: How to prove it ? (Problem 2.49)

## Slide 39: System Stability—Example 9.20
§9.7 LTI System Analysis Using Laplace Transform
Q: Statement #2 valid?
Not causal!

## Slide 40: System Stability—2nd Order System
System function
If the system is causal
a) ζ<-1, 2 right-half-plane real poles
b) -1<ζ<0, 2 right-half-plane conjugate poles
c) 0<ζ<1, 2 left-half-plane conjugate poles
d) ζ>1, 2 left-half-plane real poles
§9.7 LTI System Analysis Using Laplace Transform
Unstable
Unstable
Stable
Stable

## Slide 41: System Function of LTI System
LTI system described by Nth-order linear constant-coefficient differential equation
Apply Laplace transform to both sides
By linearity property
System function
§9.7 LTI System Analysis Using Laplace Transform
Q1: Does DE itself specify the LTI system?
Q2： CausalityROC?

## Slide 42: System Function of RLC System
§9.7 LTI System Analysis Using Laplace Transform
Q1: ROC?
Q2: Stable?

## Slide 43: Example 9.25
LTI system
Apply Laplace transform
By definition
ROC of Y(s) must contain the intersection of ROC of X(s) and ROC of H(s) (Convolution Property)
  Discussion: 3 possible choices of ROC of H(s)
§9.7 LTI System Analysis Using Laplace Transform
ROC?

## Slide 44: Example 9.26
(1)
(2) eigen-value
(3)initial-value theorem
§9.7 LTI System Analysis Using Laplace Transform

## Slide 45: Interconnections of LTI Systems
Series connection
Parallel connection
§9.8 System Block Diagram

## Slide 46: Feedback Connection
Feedforward/Open-loop transfer function H1(s)
Feedback transfer function H2(s)
Loop transfer function H1(s) H2(s)
Closed-loop transfer function H1(s) /[1+H1(s) H2(s)]
§9.8 System Block Diagram
Q: How to derive it?

## Slide 47: 1st-order Integrator
§9.8 System Block Diagram
(a)
(b) Feedback connection

## Slide 48: 2nd-order Filter (no zero)
§9.8 System Block Diagram

## Slide 49: 2nd-order Filter (2 poles, 2 zeros)
§9.8 System Block Diagram

## Slide 50: Summary
Why Laplace transform?
Laplace transform = integral + ROC
ROC and poles
Inverse Laplace transform—still keep watch on ROC

## Slide 51: Unilateral Laplace Transform
Unilateral Laplace Transform
unilateral Laplace transform pair
Unilateral L-transform can be used to analyze causal systems, especially linear systems defined by constant-coefficient DEs
  especially usefully for system response analysis with none-zero initial states
§9.9 Unilateral Laplace Transform

## Slide 52: Unilateral L-Transform vs. Bilateral L-Transform
Unilateral Laplace Transform
Bilateral Laplace Transform
§9.9 Unilateral Laplace Transform
Unilateral Laplace Transform: L-transform or right-sided signal  ROC: right-sided plane

## Slide 53: Eg. 9.32
§9.9 Unilateral Laplace Transform

## Slide 54: Eg. 9.33
§9.9 Unilateral Laplace Transform

## Slide 55: Eg. 9.35
Bilateral Laplace Transform
Unilateral Laplace Transform
§9.9 Unilateral Laplace Transform
Q: How about t<0?
A: Not specified!

## Slide 56: Convolution Property of Unilateral L-Transform
for all t<0, x1(t)=0, x2(t)=0
If either x1(t) or x2(t) is nonzero for t<0, the convolution property does NOT hold
§9.9 Unilateral Laplace Transform

## Slide 57: Eg. 9.37
LTI system described by differential equation
Unilateral L-transform of system function
Input signal
Unilateral L-transform of output signal
Inverse unilateral L-transform gives the output signal
§9.9 Unilateral Laplace Transform

## Slide 58: Differentiation Property
Unilateral Laplace transform of first-order differentiation
Unilateral Laplace transform of second-order differentiation
§9.9 Unilateral Laplace Transform
Different from bilateral L-transform case

## Slide 59: Eg. 9.38
LTI system described by differential equation
Input signal
Non-zero initial conditions: y(0-)=β, y’ (0-)=γ
Apply unilateral L-transform to both sides of DE system function
The last term corresponds to zero-state response (Eg. 9.37)
The first two terms correspond to zero-input response
A numerical example α=2, β=3, γ=-5
Inverse unilateral L-transform gives the output signal
§9.9 Unilateral Laplace Transform