## Slide 1
荷塘雨课堂
播放ppt
腾讯会议
双向语音/视频交流
2. 开启腾讯会议（请保持静音，一般关闭摄像头，发言前解除静音）
1. 开启荷塘雨课堂（请关闭音频输出，可以点名、白板、做题、弹幕等）
雨课堂可以看ppt，腾讯会议可以看现场板书，
建议分别用两个终端打开。

## Slide 2: Chapter 7 Sampling

## Slide 3: Outline
Sampling Theorem
  Impulse sampling
  Nyquist sampling theorem
Reconstruction Using Interpolation
Undersampling and Aliasing

## Slide 4: Why Sampling?
Continuous-time signal: x(t)
Discrete-time signal: x[n]
Advantages of processing discrete-time signals compared to processing continuous-time signals?
  low cost, programmable, reproducible, by using CPU/DSP/GPU/NPU…
Samples: the values of a continuous-time signal at points equally spaced in time
Sampling theorem
  Defines the conditions with which a continuous-time signal can be completely reconstructed from a sequence of its samples
  the bridge between continuous-time signals and discrete-time signals
§7.1 Sampling Theorem

## Slide 5: What if Sampling Theorem NOT Satisfied
Without certain constraints, an arbitrary continuous-time signal can NOT be reconstructed from its samples
§7.1 Sampling Theorem
x1(kT)=x2(kT)=x3(kT)

## Slide 6: Necessary Conditions for Signal Reconstruction
To completely reconstruct a continuous-time signal from a sequence of its samples
The signal is band limited: its Fourier transform is zero outside a finite band of frequencies
The sampling space is sufficiently small in comparison with the highest frequency
Sampling theorem: if the above conditions are satisfied, the samples uniquely specify the original signal
  What is a “sufficiently small” sampling space?
§7.1 Sampling Theorem

## Slide 7: Impulse-Train Sampling
Impulse-train sampling: continuous-time signal x(t) multiplied by a periodic impulse train p(t)
sampling function: p(t)
sampling period: the period of sampling function
sampling frequency:
§7.1 Sampling Theorem
Q: Is impulse-train sampling time-invariant?
A: Generally not time-invariant. But…

## Slide 8: Signals in Impulse-Train Sampling
Time domain
Frequency domain
§7.1 Sampling Theorem
Xp(jω) is also periodic, period ωs =2π/T

## Slide 9: Sampling Effect in Frequency Domain (1)
x(t) is band-limited
case I: ωs>2ωM
X(jω) can be recovered from Xp(jω) by a lowpass filter
§7.1 Sampling Theorem

## Slide 10: Sampling Effect in Frequency Domain (2)
x(t) is band-limited
case II: ωs<2ωM
Aliasing happens: overlap in spectrum
X(jω) can not be recovered from Xp(jω) by a lowpass filter
§7.1 Sampling Theorem

## Slide 11: Sampling Theorem
Nyquist Sampling Theorem: x(t) is a band-limited signal with X(jω)=0 for |ω|>ωM, then x(t) is uniquely determined by its samples x(nT), n = 0, ±1, ±1, ±2, …, if ωs>2ωM, in which ωs=2π/T.
  Nyquist rate: 2ωM
  Nyquist frequency: ωs/2
The original signal can be reconstructed from x(nT) by passing the impulse train, for which the impulses have the amplitudes of x(nT), through an ideal lowpass filter
§7.1 Sampling Theorem

## Slide 12: Reconstruction Using Ideal Lowpass Filter
cut-off frequency of ideal lowpass filter ωC: ωM<ωC < ωs - ωM
§7.1 Sampling Theorem

## Slide 13: Sampling with a Zero-Order Hold
§7.1 Sampling Theorem

## Slide 14: Equivalent Model of Sampling with Zero-Order Hold
a LTI system with the rectangle impulse response h0(t)
§7.1 Sampling Theorem
Q: Is zero-order hold sampling time-invariant?

## Slide 15: How to Reconstruct from Zero-Order Hold?
Ideally, should be a lowpass filter
The ideal reconstruction filter is given by
§7.1 Sampling Theorem
?
Discussion: What if no reconstruction filter?

## Slide 16: Interpolation
Interpolation: fitting of a continuous-time signal to a set of sample values
Linear interpolation: adjacent points are connected by straight lines
High-order interpolation: adjacent points are connected by high-order polynomials or other mathematical functions
§7.2 Reconstruction Using Interpolation
Matlab function interp1()
Q: How to differentiate between CT and DT signals in Matlab?

## Slide 17: Reconstruction = Interpolation
xr(t)=xp(t)*hr(t)
§7.2 Reconstruction Using Interpolation
-- interpolation

## Slide 18: Band-Limited Interpolation
band-limited interpolation: if is band-limited, then is band-limited interpolation
  If Nyquist conditions are satisfied, then the band-limited interpolation uniquely reconstruct the original signal
Ideal case: is the ideal lowpass filter
Question: does have to be ?
§7.2 Reconstruction Using Interpolation

## Slide 19: Does have to be ?
§7.2 Reconstruction Using Interpolation
x(t)=sin (2π·1·t+ π/3)+ sin (2π·1.75·t+ π/4), fM=1.75
T=1/4, fs=4
fc=2
fc=2.2
fc=1.8

## Slide 20: Non-Ideal Interpolation – Zero-Order Hold
Ideal interpolation vs. Non-ideal interpolation
  vs.
zero-order hold is a rough approximation of the ideal lowpass filter, but in some applications it is sufficient
  Not continuous at the sampling points
  Example: current steering digital-to-analog converter (DAC) without reconstruction filter
§7.2 Reconstruction Using Interpolation
Q: Why does a low-resolution look smoother at a distance?
A: Lowpass effect of human eyes

## Slide 21: Non-Ideal Interpolation – First-Order Hold
First-order hold sampling is actually linear interpolation
xr(t) is continuous at the sampling points
§7.2 Reconstruction Using Interpolation

## Slide 22: Undersampling
Undersampling: sampling frequency lower than the Nyquist rate 2ωM, or signal frequency higher than the Nyquist frequency ωs/2.
Undersampling leads to aliasing
§7.3 Aliasing Effect of Undersampling

## Slide 23: Aliasing Effect on Sinusoidal Signals -- Frequency Domain
without aliasing
with aliasing
§7.3 Aliasing Effect of Undersampling

## Slide 24: Aliasing Effect on Sinusoidal Signals -- Time Domain
§7.3 Aliasing Effect of Undersampling
fs=6, x(t)=sin (2π·f0·t+ π/3)
reconstruction/interpolation using ideal lowpass filter
f0= fs/6
fr= fs/6
f0= 2fs/6
fr= 2fs/6
f0= 4fs/6
fr= 2fs/6
f0= 5fs/6
fr= fs/6
Q1: How about f0= fs?
Q2: Only frequency folded? How about phase?

## Slide 25: Aliasing Effect on Phase of Sinusoidal Signals
Aliasing  frequency folded + phase reversal
  x(t)=cos(ω0t+φ)  xr(t)=cos((ωs-ω0)t-φ)
§7.3 Aliasing Effect of Undersampling
Q1: How to explain the rotors of a helicopter rotate “reversely” or stay still?
https://www.bilibili.com/video/av4953251?from=search&seid=13023715312627628363

## Slide 26: Supplementary: Bandpass Sampling
§7.3 Aliasing Effect of Undersampling
Bandpass sampling theorem: band-limited signal which has energy in the frequency range of (ωL, ωH), can be uniquely reconstructed from its samples if

## Slide 27: Summary
Two conditions of sampling theorem
  band-limited !!!
  sampling frequency sufficiently high
Reconstruction
  Using ideal lowpass filter
  zero-order and first-order hold
Aliasing: how does it happen?