## Slide 1
荷塘雨课堂
播放ppt
腾讯会议
双向语音/视频交流
2. 开启腾讯会议（请保持静音，一般关闭摄像头，发言前解除静音）
1. 开启荷塘雨课堂（请关闭音频输出，可以点名、白板、做题、弹幕等）
雨课堂可以看ppt，腾讯会议可以看现场板书，
建议分别用两个终端打开。

## Slide 2: Chapter 11 Linear Feedback Systems

## Slide 3: Outline
Linear Feedback Systems
Applications and Consequences of Feedback
Root Locus Analysis
Nyquist Stability Criterion
Phase/Gain Margins

## Slide 4: Open-loop Control vs. Closed-Loop Control with Feedback
Open-loop control
  needs to precisely know the mathematical relationship between the controlling signal and the controlled signal
  vulnerable to disturbance
Closed-loop control with feedback
  can detect and correct the output deviation promptly
  can improve the system transfer linearity and accuracy
  can stabilize the unstable systems
§11.1 Linear Feedback Systems
http://www.bilibili.com/video/BV1DW411x74c?from=search&seid=14916568497393913519

## Slide 5: Feedback in Analog Circuit Design
Feedback is used in almost all the analog circuits
Negative feedback
  reference generation
  voltage regulator
  active analog filters
  common-mode feedback
  Pipelined ADC/Successive-Approximation (SAR) ADC
  oversampling ADC
Positive feedback: clock generators, oscillators
§11.1 Linear Feedback Systems

## Slide 6: Reference generation (Bandgap)
§11.1 Linear Feedback Systems
W. Sansen, Analog Design Essentials

## Slide 7: Voltage Regulator
§11.1 Linear Feedback Systems

## Slide 8: Active Analog Filters
§11.1 Linear Feedback Systems
3rd Order Bessel Low-Pass Filter

## Slide 9: Common-Mode Feedback
§11.1 Linear Feedback Systems
W. Sansen, Analog Design Essentials

## Slide 10: Successive-Approximation (SAR) ADC
§11.1 Linear Feedback Systems

## Slide 11: Oversampling ADC
§11.1 Linear Feedback Systems

## Slide 12: General Configuration of CT LTI Feedback System
Only consider the causal systems
H(s): forward path transfer function, or open-loop transfer function
G(s): feedback path transfer function
H(s)∙ G(s): loop transfer function
: closed-loop transfer function
e(t): error signal
§11.1 Linear Feedback Systems
Q: How to get Q(s)?

## Slide 13: General Configuration of DT LTI Feedback System
Only consider the causal systems
H(z): forward path/open-loop transfer function
G(z): feedback path transfer function
: closed-loop transfer function
e[n]: error signal
§11.1 Linear Feedback Systems

## Slide 14: Application of Feedback #1: Inverse System Design
Let the forward path transfer function to be a simple gain K
If K is sufficiently large,
§11.2 Applications and Consequences of Feedback
Inverse System

## Slide 15: Inverted Feedback with Operational Amplifier
What’s the error signal?
Not easy to map it to the typical feedback configuration!
§11.2 Applications and Consequences of Feedback

## Slide 16: Thévenin Equivalent
§11.2 Applications and Consequences of Feedback

## Slide 17: Inverted Feedback with Operational Amplifier (cont’)
Forward path:
Feedback path:
Closed-loop:
Overall transfer function:
§11.2 Applications and Consequences of Feedback

## Slide 18: Inverse System Example
Overall transfer function =-  Integrator
Intuitive explanation:
  , in which P(s) is a differentiator, since for a capacitor
  The inverse system is then an integrator (inverse of differentiator)
§11.2 Applications and Consequences of Feedback

## Slide 19: Application of Feedback #2: Compensation for Nonideal Elements
If the feedback network is a gain stage K
  Usually K≤1 with passive feedback network
  K can be very linear and accurate
    especially in integrated circuits which provide good passive element matching
Closed-loop frequency response
  if
  It is allowed that is not linear, but must provide sufficient amplification gain over the desired frequency band
Advantage: the closed-loop gain accuracy is guaranteed by K
Disadvantage: gain loss, the open-loop gain is much higher than the closed-loop gain
§11.2 Applications and Consequences of Feedback

## Slide 20: Extra Analysis: How the Closed-Loop Gain is Stabilized
Basic assumptions:
  Ideal open-loop gain Aop
  Open-loop gain error Aop
  Actual open-loop gain Aop’
  Relative open-loop gain error:
Loop feedback gain: F
Ideal closed-loop gain:
Actual closed-loop gain:
Relative closed-loop gain error:
§11.2 Applications and Consequences of Feedback
Q: What if F has error?

## Slide 21: 1st Order System with Feedback
Feedforward/open-loop TF:
Feedforward/open-loop bandwidth:
Feedforward/open-loop gain-bandwidth product (GBW):
Feedback gain: K
Loop transfer function:
Loop BW:
Loop GBW:
Closed-loop transfer function:
Closed-loop BW:
Closed-loop GBW:
§11.2 Applications and Consequences of Feedback
Gain-Bandwidth Exchange
Q: Bode plot?

## Slide 22: Application of Feedback #3: Stabilization of Unstable Systems
1st order with proportional feedback
  open-loop unstable if a≥0
  closed-loop , stable if Kb>a
2nd order with proportional feedback
  open-loop unstable
    a>0, two poles on jω axis, impulse response u(t)  oscillator
    a<0, two poles, one on right-half plane
  closed-loop , still unstable
§11.2 Applications and Consequences of Feedback

## Slide 23: Application of Feedback #3: Stabilization of Unstable Systems (cont’)
2nd order with proportional-plus-derivative feedback s
  open-loop unstable
  closed-loop stable if and
( is stable with a positive damping ratio )
§11.2 Applications and Consequences of Feedback

## Slide 24: Stabilization of Unstable DT System
y[n] represents the number of animals in the nth generation
if birthrate is larger than 1, eg., y[n]=2 y[n-1] +x[n], , one pole (=2) outside unit circle, unstable
  x[n]: external influence such as migration or disease
  must be introduced to stabilize it
y[n]=2y[n-1]+e[n], e[n]=x[n]-r[n]
  r[n]: regulative control
Example: y[n]=2y[n-1]+e[n], e[n]=x[n]-r[n], r[n]=2βy[n-1]  feedback configuration
§11.2 Applications and Consequences of Feedback

## Slide 25: Stabilization of Unstable DT System (cont’)
open-loop:
feedback:
closed-loop: , stable if , or
§11.2 Applications and Consequences of Feedback

## Slide 26: Tracking Systems with Feedback
system function to be controlled
compensator for stability and other consideration
Let
e[n]: tracking error
closed-loop transfer function:
error transfer function:
To track the input, needs to minimized, should be large
§11.2 Applications and Consequences of Feedback
Q: How to prove?

## Slide 27: Tracking Systems with Feedback (Cont’)
Consider disturbance d[n]
Disturbance transfer function , which also needs to be minimized
However,
Design challenge: both and need to be minimized (?!)
Usually is low-pass
  is high-pass
  is low-pass  track the low-frequency input change, but also track the low frequency disturbance
§11.2 Applications and Consequences of Feedback

## Slide 28: A Typical Tracking System: Phase-Locked Loop (PLL)
§11.2 Applications and Consequences of Feedback
PD
Loop Filter
1/N
Ref
VCO
Phase-Locked Loop
LO

## Slide 29: Functional Blocks in PLL
Phase detector (PD): find difference between phase of two signals
Loop filter: provide appropriate control voltage for voltage-controlled oscillator (VCO)
VCO: generate signals with phase determined by the control voltage
Divide-by-N: LO phase changes N times faster than Ref phase
§11.2 Applications and Consequences of Feedback
PD
Loop Filter
1/N
Ref
VCO
Phase-Locked Loop
LO

## Slide 30: Charge Pump PLL
The charge pump PLL is one of the most popular PLL structures since 1980s
Featured with a digital phase detector and a charge pump
Advantages
  Fast lock and tracking
  No false lock
§11.2 Applications and Consequences of Feedback
Phase
Detector
Charge
Pump
Loop
Filter
VCO
N-Divider
fi
fo
fo

## Slide 31: Modeling Charge Pump PLL
§11.2 Applications and Consequences of Feedback
Phase
Detector
Charge
Pump
Loop
Filter
VCO
N-Divider
fi
fo
fo
Ip
VC
C1
R

## Slide 32: 2nd Order PLL Transfer Function
Using a 1st order LPF: Active PI type
Open-loop transfer function
Closed-loop transfer function
§11.2 Applications and Consequences of Feedback

## Slide 33: Transient Response of PLL (1)
§11.2 Applications and Consequences of Feedback
Transient response with frequency step (phase ramp)

## Slide 34: Transient Response of PLL (2)
§11.2 Applications and Consequences of Feedback
Transient response with phase jump/step

## Slide 35: Destabilization Caused by Feedback
Destabilization: negative feedback  positive feedback
Example: self-excitation of audio system
  e-sT is the system function of delay network
  unstable if K1K2>1
§11.2 Applications and Consequences of Feedback

## Slide 36: Root Locus
Root locus: graphical representation of closed-loop poles of a rational system as a function of the gain
In Matlab, rlocus() draws the root locus with the gain ranging from 0 to +∞
Example:
Let and , use Matlab to draw the root locus
§11.3 Root-locus Analysis
>0
0
Q: Replace z by s?
A: No difference in root locus

## Slide 37: Equation for Closed-Loop Poles
If no pole-zero cancellation, the closed-loop poles are given by
§11.3 Root-locus Analysis

## Slide 38: End Points of Root Locus
start point K=0  , the solutions are the poles of
K  , the root locus approach the zeros of as K
  If the order of numerator of is lower than the order of the denominator, then some branch(es) of the root locus approach the infinity as K
§11.3 Root-locus Analysis

## Slide 39: Angle Criterion
Angle Criterion: , K is real  is integer multiple of π if is on the root locus
Method to check if a specific is the closed-loop pole for a certain K
  If =odd multiple of π, then is on the root locus for some value K>0 ()
  If =even multiple of π , then is on the root locus for some value K<0 ()
§11.3 Root-locus Analysis

## Slide 40: Example to Use Angle Criterion
, G
  s0 real: (1) >-1, (2) <-2, (3) [-2, -1]
  s0 complex:
    upper half-plane:
§11.3 Root-locus Analysis
0
0

## Slide 41: Properties of Root Locus
Property 1: if has n poles, then the root locus has n branches, with each starting (for K=0) from one of the n poles
Property 2: as |K|∞, each branch of the locus approaches a zero of . If the number of zeros is less than that of the poles, some branches approaching to the infinity
Property 4: Branches of the root locus between two real poles must break off into the complex plane for |K| large enough
§11.3 Root-locus Analysis

## Slide 42: Properties of Root Locus (Cont’)
Observation #1: if a real number is to the left of one of the poles and zeros, then the contribution of that pole or zero to is –π or +π
Observation #2: for a real number , the contribution of a conjugate pole/zero pair to is 2π or 0
Property 3: (Based on the Angle Criterion) parts of the real axis lie to the left of an odd number of real poles and zeros are on the root locus for K >0
  parts of the real axis lie to the left of an even number of real poles and zeros are on the root locus for K <0
§11.3 Root-locus Analysis

## Slide 43: Example (1) of Root Locus Properties
real poles: -2, -1, real zero: 1
<-2 is on the root locus for K >0
-2<<-1 is on the root locus for K <0
-1<<1 is on the root locus for K >0
>1 is on the root locus for K <0
§11.3 Root-locus Analysis
0
0
stable
Q: K?

## Slide 44: Example (2) of Root Locus Properties
§11.3 Root-locus Analysis
0
<0
For stability:

## Slide 45: Root locus of 2nd-order loop*
Loop transfer function (without gain stage)
Closed-loop transfer function
Pole(s) of are zero(s) of
If is on the root locus,


§11.3 Root-locus Analysis

## Slide 46: Root locus of 2nd-order loop (cont’)
Note that



 the real axis is part of the root locus


The root locus includes a circle centered at (c, 0) with radius
§11.3 Root-locus Analysis

## Slide 47: Encirclement Property
rational function W(p), p is a complex variable
  for CT case, p is s
  for DT case, p is z
traverse a closed contour in the p-plane in the clockwise direction, and plot W(p) in the W-plane
Encirclement Property: As a closed contour C is traversed once in the clockwise direction, the corresponding plot of W(p) encircles the origin in the clockwise direction n times, with n = number of zeros - number of poles contained within C
  if n<0, plot of W(p) encircles the origin in the counterclockwise direction |n| times
§11.4 Nyquist Stability Criterion

## Slide 48: Example of Encirclement Property
§11.4 Nyquist Stability Criterion

## Slide 49: Stability Requirement of CT LTI Feedback Systems
Open-loop H(s), feedback path G(s)
Closed-loop
Closed-loop poles are zeros of
  poles of are zeros of
Stability requires that no zeros of lie in the right half-plane in the s-plane
§11.4 Nyquist Stability Criterion

## Slide 50: Contour Equivalent to Right Half-Plane
Construct a clockwise closed contour C
When M goes to infinity
  the contour C is extended to the right half-plan
  the contour C becomes –jM to jM
§11.4 Nyquist Stability Criterion

## Slide 51: CT Nyquist Stability Criterion
Use Encirclement Property: number of zeros – number of poles of 𝑅(𝑠)=1/𝐾+𝐺(𝑠)𝐻(𝑠) on the right half-plane = number of clockwise encirclements of the origin by 𝑅(𝑠) for
  poles of 𝑅(𝑠) are poles of 𝐺(𝑠)𝐻(𝑠)
  zeros of 𝑅(𝑠) are the closed-loop poles
    For stability, number of zeros 𝑅(𝑠) on the right half-plane must be 0
number of clockwise encirclements of the origin by 𝑅(𝑠) = number of clockwise encirclements of the -1/K by 𝐺(𝑠)𝐻(𝑠)
CT Nyquist Stability Criterion: the net number of clockwise encirclements of -1/K by 𝐺(𝑠)𝐻(𝑠) must equal minus the number of right-half-plane poles of 𝐺(𝑠)𝐻(𝑠)
  the number of counterclockwise encirclements of -1/K by 𝐺(𝑠)𝐻(𝑠) must equal the number of right-half-plane poles of 𝐺(𝑠)𝐻(𝑠)
  If both 𝐺(𝑠) and 𝐻(𝑠) are stable the number of encirclements of -1/K by 𝐺(𝑠)𝐻(𝑠) must equal 0
  If either 𝐺(𝑠) or 𝐻(𝑠) is unstable…..
§11.4 Nyquist Stability Criterion
Q1: Why?
Q2: Why?

## Slide 52: Example (1) of CT Nyquist Stability Criterion
,
Both 𝐺(𝑠) and 𝐻(𝑠) are stable the number of encirclements of the -1/K by 𝐺(𝑠)𝐻(𝑠) must equal 0
For stability: -1/K≤0 or -1/K>1  K≥0 or -1<K<0
§11.4 Nyquist Stability Criterion
Nyquist Plot

## Slide 53: Example (2) of CT Nyquist Stability Criterion
not stable!
The number of counterclockwise encirclements of the -1/K by 𝐺(𝑠)𝐻(𝑠) must equal the number of right-half-plane poles of 𝐺(𝑠)𝐻(𝑠)
For stability, -1<-1/K<0  K>1
§11.4 Nyquist Stability Criterion

## Slide 54: Extra Discussion on Nyquist Stability Criterion
How if the poles of are on the axis?
  values of are infinity on these points
  Nyquist stability criterion can be modified to allow poles of on the axis
  How if is not rational?
    If both and are stable, then the Nyquist Criterion can still be used
    No encirclement of -1/K by 𝐺(𝑠)𝐻(𝑠)
§11.4 Nyquist Stability Criterion

## Slide 55: Example (3) of CT Nyquist Stability Criterion
Nyquist plot: infinity number of encirclements of the origin by 𝐺(𝑠)𝐻(𝑠) as varies from -∞ to +∞
For stability: -1/K<-1 or -1/K>1  |K|<1
§11.4 Nyquist Stability Criterion

## Slide 56: DT Nyquist Stability Criterion
For the closed-loop system to be stable, the net number of clockwise encirclements of -1/K by the Nyquist plot of must equal minus the number of poles of that lie outside the unit circle
§11.4 Nyquist Stability Criterion

## Slide 57: Gain Margin and Phase Margin
Gain margin: the minimum additional gain K (φ=0) to make the closed-loop system unstable
Phase margin: the minimum additional phase φ (K=1) to make the closed-loop system unstable
§11.5 Phase and Gain Margins

## Slide 58: Alternative Definitions of Gain Margin and Phase Margin (Bode Plot)
In the Bode plot of
Gain Margin: the difference between and 0 dB for the frequency that makes
  calculated as
Phase Margin: the difference between and or for the frequency that makes (assume < )
  calculated as , if
  calculated as , if
§11.5 Phase and Gain Margins

## Slide 59: Stability Analysis Based on Bode Plot
§11.5 Phase and Gain Margins
Phase Margin=48.92°
Note: extra 180 phase shift with negative feedback

## Slide 60: Summary
Advantage of negative feedback
  improve linearity and accuracy, stabilization, ….
  What’s the cost?
1st order feedback equation
Root locus for stability analysis
Nyquist Criterion for stability analysis
Gain margin/Phase Margin for stability analysis